## Slide 1
At the basic level a cell phone is just a two-way radio.
It requires one channel or frequency to transmit and one channel or frequency to receive.
Cell phones can both send and receive at the same time, unlike a walkie-talkie that uses a single channel to send and receive where you have to wait your turn and push the button to send.
The reason that there is a requirement for radio frequency reuse planning is both simple and practical
The Federal Communications Commission, (FCC) allots a limited number of radio frequencies to each wireless company.
The number of frequencies available is far too small to accommodate millions of phone calls at the same time.
In order to compensate for this lack of radio frequencies, wireless companies use technology that allows them to split the frequencies into small sections
This allows more phones to use the frequencies than would be possible if a phone took up the entire radio channel.
Two primary methods for “sharing” radio channels are
  Time Division Multiple Access (TDMA) which is used in the Global System for Mobile Communications (GSM) network
    AT&T, T-Mobile & rest of the world
  Code Division Multiple Access (CDMA) used in the CDMA network
    Sprint, Verizon, and US Cellular

## Slide 2
GSM
2G GSM 900 & 1800 MHz
GSM 900 MHz frequency
  Uplink 890 – 915 MHz(25 MHz)
  Downlink 935 – 960 MHz (25 MHz)
  25 MHz / 200 KHz
  125 frequencies
  200 KHz (2 * 100 KHz) as Guard band
  124 usable frequencies
  1st frequency is located at 890.2 MHz (+/- 100 KHz)
  Eight time slots per frequency
  Allows 8 full-rate speech channels per radio frequency
  These eight slots (burst periods) are grouped into a TDMA frame
  Half-rate channels use alternate frames in the same timeslot.
  The channel data rate for all 8 channels is 270.833 kbit/s,
  The frame duration is 4.615 ms
  4.615*8 = 36.92
  1000/36.92 = 27.09 Hz
Absolute Radio Frequency Channel Number (ARFCN)
  Upload/download link frequency pairs
Duplex spacing/duplex distance
  Difference between paired uplink/downlink frequencies
  Typically 45MHz on

## Slide 3
CDMA
Each user in a CDMA system uses a different code to modulate their signal.
Choosing the codes used to modulate the signal is very important in the performance of CDMA systems.
The best performance occurs when there is good separation between the signal of a desired user and the signals of other users. The separation of the signals is made by correlating the received signal with the locally generated code of the desired user.
If the signal matches the desired user's code, then the correlation function will be high and the system can extract that signal.
If the desired user's code has nothing in common with the signal, the correlation should be as close to zero as possible (thus eliminating the signal); this is referred to as cross-correlation.
If the code is correlated with the signal at any time offset other than zero, the correlation should be as close to zero as possible.
This is referred to as auto-correlation and is used to reject multi-path interference.
An analogy to the problem of multiple access is a room (channel) in which people wish to talk to each other simultaneously.
To avoid confusion, people could take turns speaking (time division), speak at different pitches (frequency division), or speak in different languages (code division).
CDMA is analogous to the last example where people speaking the same language can understand each other, but other languages are perceived as noise and rejected.
Similarly, in radio CDMA, each group of users is given a shared code. Many codes occupy the same channel, but only users associated with a particular code can communicate.

## Slide 4
VoLTE
Voice Telephony is of two types -
Circuit Switched, and
Packet Switched.
Existing 2G, 3G and non-Jio 4G networks use circuit switched technology for voice.
Research POTS vs 2, 3, 4, 5G

## Slide 6
Home Location Registry (HLR)
Subscriber-specific information such as:
International mobile Subscriber Identifier (IMSI)
International Mobile Equipment Identifier (IMEI)
Current/last known location of cell phone
Roaming restrictions
Subscriber supplemental features
Visitor Location Registry (VLR)
Roaming-subscriber information
Autonomous registration
When a roaming phone goes into an area not covered by its carrier it registers with HLR and is added to VLR
Happens from time-to-time automatically
Disconnect
When a phone leaves an area no specific disconnect signal is sent
When phone shuts down a “kiss-off” signal is sent

## Slide 7
Calls/Connections
When a cell phone is turned on, it registers with the cellular system by contacting the network via a signaling/control and paging channel.
This channel used by phone to announce its presence to network.
The phone is allowed to access network for its carrier.
Features for that subscriber plan will be activated
The registration system allows cellular system to know how to find the cell phone when system needs to route a call to phone
Data storage of these registration pings is only present for a few hours and are not recoverable after the fact
Making a call. Bob calls Sue.
  Bob’s cell phone scans for best signal from a tower
  MSC verifies Bob is valid subscriber, checks for available channel
  MSC asks HLR for Sue’s account and location
  The call is sent to the last tower that Sue’s phone pinged
  The tower sends call to Sue
GSM
Periodically pings tower with strongest signal
Camps on tower til stronger signal found
Tower selection made in ‘idle’ mode (not during a call)
Once phone in a call the network will handle the tower selection vis “handoffs”
CDMA
Phone itself sends PREP (Pilot Reports) reports on tower signal strength
Phone does this when idle and in call
Phone performs this function telling network what cell sire to send its traffic over
Types of call
Completed
Call attempt, no answer, caller gives up
Routed call, no answer – the phone cannot be reached
Forwarded call

## Slide 9
Cell Towers, Cell Sites
Cell Site: remote buildings with cellular radio equipment and antennas on towers
Beam width 120
Can be narrower (longer). Horizontal Beam width
Azimuth is direction radio antennas pointed
Cell Towers do NOT have an “average” coverage area
Co-located antennas from multiple companies
Antennas send and receive signals to and from phones
Base Transceiver Station (3G) and eNode B (4g LTE) manage the tower and calls on the tower.
Talks to phone network via cables.
Plain Old Telephone System (POTS)
Newer non-POTS technology
  Integrated Digital Services Network (ISDN)
  Digital Subscriber Line (DSL)
  Fiber Distributed Data Interface (FDDI)

## Slide 10
Phone Locations
Call details records
  Cell tower and sector used by cell phone on a map
Real-time Call details records
  Warrant required
  Bear in mind this does not record pings, user needs to make/receive calls
“Precision location” data (Comes in three forms normally). These are engineering tools to check health of networks, not accurate for phone locations
  Per Call Measurement Data (PCMD) Sprint
    Based on Round Trip Delay (RTD)… Signal from tower-phone-tower
    Periodic timing measurements from three sites to triangulate position
    Not reliable because timings are affected by
      Multipathing extends distance
      Capacity issues
      Multiple hand-off connections
      Repeaters
      Also, Minimum 3 towers signaling phone
  Real Time Tool (RTT) Verizon
    Also based on Round Trip Delay (RTD)… Signal from tower-phone-tower
  Network Event Location System (NELOS) AT&T
    GPS technology
  These are engineering tools to check health of networks, not accurate for phone locations
Cellular data pings
  real-time geolocation tracking of cellular phone by activating E911 system
  Subsequently uses a network-based or handset-based method for triangulating cell phone
  Gives estimated location of phone itself
Drive testing
  Drive around with specialized equipment testing tower connections during calls
  Be aware this data may be used in court even if we don’t do it ourself
Emergency 911 System
  To provide geo-location to emergency services
  FCC’s basic 911 rules require wireless service providers to transmit all 991 calls to a Public Safety Access/Answering Point (PSAP)
  A primary PSAP is defined as a PSAP to which 9-1-1 calls are routed directly from the 9-1-1 Control Office, such as, a selective router or 9-1-1 tandem
  Phase I 911 rules: Must provide cell number and Cell Site of 911 call
  Phase II 911 rules: Must ALSO provide latitude and longitude of caller
  Requires a 45s phone call for geolocation
  Enhanced 911, Law enforcement request ping of phone to track it

## Slide 11
Records
Call detail records can show which cell tower, and sector were used for a phone call
AT&T can show which tower was used for text and data BUT data transmission time stamps are one hour apart and, therefore, not discrete in the time-domain as the actual time of the data transmission within that hour is not known
As a result data transmissions and phone calls may be shown the records to be taking place at DIFFERENT towers
Data transmission continues even if the user is NOT interacting with the phone
AT&T likely to be only company that has usable text/sms & tower data
Text content often kept by wireless company for a few days
Which Tower
Cell phones attempt to connect to tower emitting the highest quality signal at a given moment, not only the closest.
The actual determination of which tower was connected to is complex, hinges on a multitude of factors, none of which are memorialized in the cell records
Rayleigh and Rician fading, multipath, diffraction
Factors may include:
  Available capacity of tower at time (sport/live event nearby)
  Tower health/functionality at time (get outage data)
  Line of sight from phone to cell tower
  Radio signal interference from other towers
  Signal reflection/diffraction from buildings
  Signal scattering
  Blocking signal
Dominant vs non-dominant regions of overlapping cell tower strength

## Slide 12
Call Detail Records
Most common type of evidence
Common to every carrier and can be obtained after the fact
Network traffic for cell phone transactions is collected by Mobile Switching Centers (MSCs)
Call records generated as a result of a query of this database and put into a report
Business reasons for collecting this data
Proof of service/Customer service/disputes
Transaction record for financial accounting
Technical picture of each transaction
Data contained in Cell Phone Records
Note: Dialed number may contain speed dials
Records may look different for CDMA vs GSM
CDMA records
First cell tower phone call went through and possibly last
Will NOT contain tower info for text messages or data transmissions
Sector numbers for records in CDMA networks for Lucent switches are numbered differently than for Nortel or Ericsson
GSM records
AT&T 1st tower and possibly additional towers in a call (chosen in idle mode)
After the first tower subsequent towers are chosen by the network and are unreliable location indicators
To obtain from wireless company you need to request
  Call detail records
  Cell tower location records
Can request maintenance and outage records from wireless company’s subpoena compliance dept
See page 43 in “Cell Phone Location Evidence for Legal Professionals” book for example subpoena

## Slide 13
How cell phone location evidence is presented in court
Maps are key
When an analyst tries to show coverage area of a cell tower… unless they are using radio propagation maps created by wireless telephone company they are taking a risk
There is NO way to determine the coverage of a cell tower sector through the use of call detail records.
Coverage area of a cell tower should never be part of an analyst’s mapping or court presentations unless that information comes
  directly from the wireless telephone company in the form of a radio propagation map
  or drive testing contemporaneous to the date in question
Coverage area: the area around the cell tower where the radio waves reach the ground
A single cell site can contain the hardware for several cells, which are then also known as sectors.
The sectors will operate independently of each other having unique IDs
NO knowledgeable expert should be using pie slices
Be no more detailed than this

## Slide 14
Record Open Date/Time | Record Open Dt/Tm(GMT) | SID | NID | Cell ID | Cell Face | Market ID | eNB ID | Dir | MSISDN | Called # | CPN | SOU | RAT | ENDPOINT | VZWNE/V4B | User Equip Type
2020/03/29 18:49:42(GMT -5) | 3/29/2020 23:49 | N/A | N/A | N/A | 34 | 121 | 121002 | MT | ??????? | ??????? | ??????? | 13 | LTE | N/A | N/A | 3.55E+15
Site Number | E-911 Latitude | E-911 Longitude | Street Address | City | State | Zip | Sector | Azimuth (deg) | Antenna H-BW (deg) | Channel Type | eNodeB ID | Vendor
2 | 30.343027 | -95.0788 | 120 Peach Ave # A | Cleveland | TX | 77327 | 3 | 270 | 61.25 | LTE | 121002 | Nokia
Verizon Call data
Excel sheet 1: call data
Excel sheet 2: site data
The call
The site
Change my code to use this

## Slide 15
Sectors (usually 3)
Orientation/Rotation
Azimuth
3 (gamma)
2 (beta)
1 (alpha)
cell tower
We can add multiple addresses:
incident address (i)
alibi address
If a call was made at time of an ‘incident’ we can determine the sector call was made from